## Slide 1
Direct Stiffness Method Program for 3D Structural Analysis
A Simplified DSM Solver and Validation Example
Siyuan Wang | CEE6501 | 04/24/2026

## Slide 2
Project Objective and Workflow
Overview
A Direct Stiffness Method program is developed for 3D truss, frame, and hybrid truss-frame systems.
A JSON input file is used to define geometry, supports, materials, sections, and loading.
One consistent pipeline is followed: read input → element routines → assembly → partition → solve → postprocess.
Displacement, reaction, and member-force tables are exported, and the deformed shape is visualized in the notebook.
JSON Input
Element Quantities
Global Assembly
Partition
Solve
Postprocess

## Slide 3
Validation Strategy
The code is checked feature by feature before it is used for the final bridge model.
Truss Validation (4 cases)
Nodal loads
Support displacement
Temperature load
Fabrication error
Frame Validation (6 cases)
Nodal moments
Distributed member loads
Moment release
Support displacement
Temperature load
Fabrication error
Why Validation?

## Slide 4
Truss Validation I: Nodal Loads and Support Displacement
Nodal Loads
Node 11:
Node 12:
Key check: reactions balance the applied forces
Observed behavior: reaction sums are consistent with global equilibrium
Support Displacement
Node 1: prescribed
Key check: restrained-node displacement should match the input exactly
Observed behavior: the displacement table reports the imposed value correctly
Interpretation: this validates boundary-condition handling

## Slide 5
Truss Validation II: Temperature and Fabrication Error
Temperature Load
All 43 members:
Thermal coefficient:
Expected axial strain:
Purpose: verify thermal-load assembly in the truss solver
Fabrication Error
Element 6: +0.01m length error
Element 17: -0.01m length error
Purpose: convert local incompatibility into equivalent element actions
Observed behavior: moderate redistributed displacement field

## Slide 6
Frame Validation I: Nodal Moments and Member Loads
Nodal Moments
Selected Mx and My nodal moments are applied at intermediate floors
Purpose: show directional deformation in the 3D frame model
The case demonstrates bending-dominated frame behavior rather than pure axial response
Distributed Member Loads
12 members:
Total applied x-direction load: 2000 kN
Key check: reactions sum to -2000 kN in Fx
Purpose: verify member-load conversion and reaction recovery

## Slide 7
Frame Validation II: Moment Release and Support Displacement
Moment Release
Use the same member-load case with selected release codes MT=1 or 2
Expected trend: the released structure becomes softer
Observed result: max displacement rises from 12.764 m to 16.353 m
Displacement increase: about 28.1%
Support Displacement
Node 1:
Node 3:
Key check: restrained-node displacements should equal the imposed values
Purpose: verify prescribed support movement in the frame solver

## Slide 8
Temperature Load
Fabrication Error
Element 5 and element 6: error = -0.01 m
Purpose: convert local incompatibility into equivalent element actions
Observed behavior: moderate redistributed displacement field
Frame Validation III: Temperature and Fabrication Error
All 43 members:
Thermal coefficient:
Expected axial strain:
Purpose: verify thermal-load assembly in the truss solver

## Slide 9
Case Study: Jiujiang Yangtze River Bridge
Three-span continuous arch-truss bridge
Total length: 576 m; span arrangement: 180 + 216 + 180 m
Modeled as a mixed truss-frame system

## Slide 10
Final Bridge Model and Load Cases
Model
Three-span continuous arch-truss bridge based on the Jiujiang Yangtze River Bridge configuration.
354 nodes and 1225 elements.
Mixed idealization: 1145 truss elements + 80 frame elements.
Load Files
Load case | Main loading description
Nodal loads only | 130 loaded nodes with concentrated downward loads (full 3 spans)
Member loads only | 350 members with (full 3 spans)
Support disp only | 4 internal support nodes with (middle 4 supports)
Temperature only | All members:
Comprehensive case | 50 nodal loads, 40 loaded members, 8 support movements, +50°C on all members

## Slide 11
Comprehensive Bridge Case: Load Balance and Key Responses
Applied Actions
50 nodal loads with total vertical load
40 loaded members with
→ total distributed vertical load
8 support movements
Uniform temperature rise: +50°C on all members
Key Results
Total applied vertical mechanical load
Support reactions sum to in z axis
Maximum total displacement: 3.2791 m at node 350
Largest vertical displacement:
at node 181

## Slide 12
Main Takeaways
Conclusion
The validation cases support the correctness of equilibrium, compatibility, thermal strain, member-load calculation, and release handling.
The hybrid solver can analyze a much larger mixed truss-frame system in one global model.
For the bridge, critical axial forces concentrate near support-adjacent truss members, while large bending moments concentrate in the arch ribs.
Questions?